## Slide 1: Sekapur Sirih Jaringan Komputer
Gandeva Bayu Satrya (GBS)
gbs@ittelkom.ac.id
gandeva.bayu.s@gmail.com
TELKOM ENGINEERING SCHOOL
Telkom University

## Slide 2: References

## Slide 3: Add. References

## Slide 4: References Details
Chapter 1 : Comp.Net & The Internet
Chapter 2 : Application Layer
Chapter 3 : Transport Layer
Chapter 4 : Network Layer
Chapter 5 : Link Layer and LANs
Chapter 6 : Wireless and Mobile Net.
Chapter 7 : Multimedia Networking
Chapter 8 : Security in Comp.Net
Chapter 9 : Network Management

## Slide 5: Rules
Use 2012’ s Curiculum
Scoring
Pre, Post, & Task (SCL) : 15%
Attitute (SCL) : 10%
Mid Test : 35%
Final Test : 40%
Penalty
Plagiarism  E
Attendance  >= 75% (Roster)

## Slide 6: CHAPTER 1 FOUNDATION
Gandeva Bayu Satrya (GBS)
gbs@ittelkom.ac.id
gandeva.bayu.s@gmail.com
TELKOM ENGINEERING SCHOOL
Telkom University

## Slide 7: Agenda
Chapter 1. Comp.Net & The Internet
1.1 Application
1.2 Requirements
1.3 Net. Architecture
1.4 Internet
1.5 Implementing Net Soft.
1.6 Performance

## Slide 8: Application
Most people know about the Internet (a computer network) through applications
World Wide Web
Email
Online Social Network
Streaming Audio Video
File Sharing
Instant Messaging
…

## Slide 9: Application
URL
  Uniform resource locater
  http://www.cs.princeton.edu/~llp/index.html
HTTP
  Hyper Text Transfer Protocol
TCP
  Transmission Control Protocol
17 messages for one URL request
  6 to find the IP (Internet Protocol) address
  3 for connection establishment of TCP
  4 for HTTP request and acknowledgement
    Request: I got your request and I will send the data
    Reply: Here is the data you requested; I got the data
  4 messages for tearing down TCP connection

## Slide 10: Agenda
Chapter 1. Comp.Net & The Internet
1.1 Application
1.2 Requirements
1.3 Net. Architecture
1.4 Internet
1.5 Implementing Net Soft.
1.6 Performance

## Slide 11: Requirement : Perspectives
Application Programmer
  List the services that his application needs: delay bounded delivery of data
Network Designer
  Design a cost-effective network with sharable resources
Network Provider
  List the characteristics of a system that is easy to manage

## Slide 12: Requirement : Connectivity
Need to understand the following terminologies
Scale
Link
Nodes
    Point-to-point
    Multiple access
Switched Network
    Circuit Switched
    Packet Switched
Store-and-forward

## Slide 13: Requirement : Connectivity
Terminologies (contd.)
  Cloud
  Hosts
  Switches
  internetwork
  Router/gateway
  Host-to-host connectivity
  Address
  Routing
  Unicast/broadcast/multicast
A switched network
Interconnection of networks
(a)
(b)

## Slide 14: Requirement : Resource Sharing

## Slide 15: Agenda
Chapter 1. Comp.Net & The Internet
1.1 Application
1.2 Requirements
1.3 Net. Architecture
1.4 Internet
1.5 Implementing Net Soft.
1.6 Performance

## Slide 16: Network Architecture
a computer network must provide general, cost-effective, fair, and robust connectivity among a large number of computers.
network designers have developed general blueprints—usually called network architectures—that guide the design and implementation of networks

## Slide 17: Network Architecture
Analogy TCP/IP OSI

## Slide 18: Protocols
Protocol defines the interfaces between the layers in the same system and with the layers of peer system
Building blocks of a network architecture
Each protocol object has two different interfaces
  service interface: operations on this protocol
  peer-to-peer interface: messages exchanged with peer

## Slide 19: Protocol Data Unit
PDU
DATA
SEGMENT
PACKET
FRAME
BITS

## Slide 20: Encapsulation, Mux, & DeMux

## Slide 21: Agenda
Chapter 1. Comp.Net & The Internet
1.1 Application
1.2 Requirements
1.3 Net. Architecture
1.4 Internet
1.5 Implementing Net Soft.
1.6 Performance

## Slide 22: 1.1 What is the Internet?
Internet: “network of networks”
  loosely hierarchical
  public Internet versus private intranet
Internet standards
  RFC: Request for comments
  IETF: Internet Engineering Task Force
  IANA : Internet Assigned Numbers Authority
  http://www.ietf.org/rfc.html

## Slide 24: Internet [Tanenbaum 2011]
The Internet is not really a network at all, but a vast collection of different networks that use certain common protocols and provide certain common services.

## Slide 25: Internet [Perterson 2012]
Internet in 1990’s
... how to connect a heterogeneous collection of networks to create an internetwork and how to use the simple hierarchy of the IP address to make routing in an internet somewhat scalable.

## Slide 26: Internet [Lammle 2005]
  The internet is defined as a global mesh of interconnected networks ...

## Slide 27: Agenda
Chapter 1. Comp.Net & The Internet
1.1 Application
1.2 Requirements
1.3 Net. Architecture
1.4 Internet
1.5 Implementing Net Soft.
1.6 Performance

## Slide 28: API
Interface exported by the network
Since most network protocols are implemented (those in the high protocol stack) in software and nearly all computer systems implement their network protocols as part of the operating system, when we refer to the interface “exported by the network”, we are generally referring to the interface that the OS provides to its networking subsystem
The interface is called the network Application Programming Interface (API)

## Slide 29: API (sockets)
Socket Interface was originally provided by the Berkeley distribution of Unix
  - Now supported in virtually all operating systems
Each protocol provides a certain set of services, and the API provides a syntax by which those services can be invoked in this particular OS.

## Slide 30: Socket
What is a socket?
  The point where a local application process attaches to the network
  An interface between an application and the network
  An application creates the socket
The interface defines operations for
  Creating a socket
  Attaching a socket to the network
  Sending and receiving messages through the socket
  Closing the socket

## Slide 31: Agenda
Chapter 1. Comp.Net & The Internet
1.1 Application
1.2 Requirements
1.3 Net. Architecture
1.4 Internet
1.5 Implementing Net Soft.
1.6 Performance

## Slide 32: Bandwidth
Bandwidth
  Width of the frequency band
  Number of bits per second that can be transmitted over a communication link
Example :
1 Mbps: 1 x 106 bits/second
meaning that it is able to deliver 10 million bits every second
Bandwidth and throughput are two of the most confusing terms used in networking. What is The Difference?
Notes: If you see the word bandwidth used in a situation in which it is being measured in hertz, then it probably refers to the range of signals that can be accommodated.
A useful distinction can also be made, however, between the maximum data rate that is available on the link and the number of bits per second that we can actually transmit over the link in practice. We tend to use the word throughput to refer to the measured performance of a system.

## Slide 33: Latency (delay)
Latency = Propagation + transmit + queue
Propagation = distance/speed of light
Transmit = size/bandwidth

## Slide 34: Delay X Bandwidth
We think the channel between a pair of processes as a hollow pipe
Latency (delay) length of the pipe and bandwidth the width of the pipe
Delay of 50 ms and bandwidth of 45 Mbps
50 x 10-3 seconds x 45 x 106 bits/second
2.25 x 106 bits = 280 KB data.

## Slide 35: Throughput
Throughput = TransferSize/TransferTime
TransferTime = RTT +1/Bandwidth ×TransferSize
Example :
where a user wants to fetch a 1-MB ﬁle across a 1-Gbps network with a round-trip time of 100 ms.
The TransferTime includes both the transmit time for 1 MB (1/1 Gbps ×1 MB = 8 ms) and the 100-ms RTT, for a total transfer time of 108 ms.
This means that the effective throughput will be
1 MB/108 ms = 74.1 Mbps

## Slide 36: Throughput (con’t)
Another Example :
Suppose one wants to stream a video that is one quarter the size of a standard TV screen; that is, it has a resolution of 352 by 240 pixels.
If each pixel is represented by 24 bits of information, as would be the case for 24-bit color, then the size of each frame would be
(352 ×240 ×24)/8 = 247.5 KB
If the application needs to support a frame rate of 30 frames per second, then it might request a throughput rate of 75 Mbps.

## Slide 37: Packet Loss
Instead, a packet can arrive to find a full queue. With no place to store such a packet, a router will drop that packet; that is, the packet will be lost.
a packet loss will look like a packet having been transmitted into the network core but never emerging from the network at the destination.
The fraction of lost packets increases as the traffic intensity increases.

## Slide 38: Bibliography
Kurose, J.F., and Ross, K.W., Computer Networking : A Top-Down Approach Sixth Edition, Pearson Education, Inc. USA, 2013.
Peterson, L.L., and Davie, B.S., Computer Networks: A Systems Approach Fifth Edition, Morgan Kaufmann, Burlington USA, 2012.
Tanenbaum, A.S., and Wetherall, D.J., Computer Networks Fifth Edition, Pearson Education, Inc., Boston USA, 2011.
Lammle T., Cisco Certified Network Associate : Study Guide Fifth Edition, Sybex, Inc. USA, 2005.

## Slide 39: THANK YOU
Gandeva Bayu Satrya (GBS)
gbs@ittelkom.ac.id
gandeva.bayu.s@gmail.com
TELKOM ENGINEERING SCHOOL
Telkom University