## Slide 1: Chapter 5 End to End Protocols
Gandeva Bayu Satrya (GBS)
gbs@ittelkom.ac.id
gandeva.bayu.s@gmail.com
TELKOM ENGINEERING SCHOOL
Telkom University

## Slide 2: Agenda
Chapter 5. End to End Protocols
E2E Protocols
Simple Demultiplexer (UDP)
Reliable Byte Stream (TCP)
RPC
RTP

## Slide 3: Internet (TCP/IP) Protocol Suite
Application layer
DHCP DHCPv6 DNS FTP HTTP IMAP IRC LDAP MGCP NNTP BGP NTP POP RTP RTSP RIP SIP SMTP SNMP SOCKS SSH Telnet TLS/SSL XMPP more...
Transport layer
TCP UDP DCCP SCTP RSVP more...
Internet layer
IP IPv4 IPv6 OSPF ICMP ICMPv6 ECN IGMP IPsec more...
Network Access layer
ARP/InARP NDP Tunnels L2TP PPP Media access control Ethernet DSL ISDN FDDI DOCSIS more...

## Slide 4: End to End Protocols
Common properties that a transport protocol can be expected to provide
  Guarantees message delivery
  Delivers messages in the same order they were sent
  Delivers at most one copy of each message
  Supports arbitrarily large messages
  Supports synchronization between the sender and the receiver
  Allows the receiver to apply flow control to the sender
  Supports multiple application processes on each host

## Slide 5: End to End Protocols
Typical limitations of the network on which transport protocol will operate
  Drop messages
  Reorder messages
  Deliver duplicate copies of a given message
  Limit messages to some finite size
  Deliver messages after an arbitrarily long delay

## Slide 6: End to End Protocols
Challenge for Transport Protocols
  Develop algorithms that turn the less-than-desirable properties of the underlying network into the high level of service required by application programs
JMM Kamal, MS Hasan, AL Griffiths, H Yu
Development and verification of simulation model based on real MANET experiments for transport layer protocols (UDP and TCP)
International Journal of Automation and Computing. Springer.
February 2013, Volume 10, Issue 1, pp 53-63
Gurmeet Singh, and Jaswinder Singh
A review of TCP Reno, TCP Vegas and TFRC for mobile ad hoc networks.
2013 IJAIR. ALL RIGHTS RESERVED, Vol. 2 Issue 4 ISSN: 2278-7844.
Nuha, H.H. ; Hendrawan, H. ; Yulianto, F.A.
Wireless Multi-path TCP Westwood+ Modification to Achieve Fairness in HSDPA
Computer Modeling and Simulation (EMS), 2010 Fourth UKSim European Symposium on
Publication Year: 2010 , Page(s): 402-407 .

## Slide 7: Agenda
Chapter 5. End to End Protocols
E2E Protocols
Simple Demultiplexer (UDP)
Reliable Byte Stream (TCP)
RPC
RTP

## Slide 8: Simple Demultiplexer
A more common approach, and the one used by UDP, is for processes to indirectly identify each other using an abstract locater, usually called a port.
The basic idea is for a source process to send a message to a port and for the destination process to receive the message from a port.

## Slide 9: User Datagram Protocol (UDP)
Extends host-to-host delivery service of the underlying network into a process-to-process communication service
Adds a level of demultiplexing which allows multiple application processes on each host to share the network
Connectionless
There is no ﬂow-control mechanism in UDP to tell the sender to slowdown.
UDP does not implement ﬂow control or reliable/ordered delivery

## Slide 10: UDP Header
UDP Header UDP Message Queue

## Slide 11: Agenda
Chapter 5. End to End Protocols
E2E Protocols
Simple Demultiplexer (UDP)
Reliable Byte Stream (TCP)
RPC
RTP

## Slide 12: Reliable Byte Stream
In contrast to UDP, Transmission Control Protocol (TCP) offers the following services
  Reliable
  Sequence and Acknowledgement
  Connection oriented
  Byte-stream service

## Slide 13: Transmission Control Protocol (TCP)

## Slide 14: Flow Control VS Congestion Control
Flow control involves preventing senders from overrunning the capacity of the receivers
Congestion control involves preventing too much data from being injected into the network, thereby causing switches or links to become overloaded

## Slide 15: TCP
As TCP runs over the Internet rather than a point-to-point link, the following issues need to be addressed by the Sliding Window Algorithm
  TCP supports logical connections between processes that are running on two different computers in the Internet
  TCP connections are likely to have widely different RTT times
  Packets may get reordered in the Internet
  TCP needs a mechanism using which each side of a connection will learn what resources the other side is able to apply to the connection
  TCP needs a mechanism using which the sending side will learn the capacity of the network
Notes: At the heart of TCP is the sliding window algorithm (discussed in Chapter 2)

## Slide 16: TCP Segment (process)
TCP is a byte-oriented protocol, which means that the sender writes bytes into a TCP connection and the receiver reads bytes out of the TCP connection.
Although “byte stream” describes the service TCP offers to application processes, TCP does not, itself, transmit individual bytes over the Internet.

## Slide 17: TCP Segment (process)
TCP on the source host buffers enough bytes from the sending process to fill a reasonably sized packet and then sends this packet to its peer on the destination host.
TCP on the destination host then empties the contents of the packet into a receive buffer, and the receiving process reads from this buffer at its leisure.
The packets exchanged between TCP peers are called segments.

## Slide 18: TCP Segment
How TCP manages a byte stream.

## Slide 19: Establishment & Termination

## Slide 20: TCP state-transition diagram

## Slide 21: Sliding Window Revisited
TCP’s variant of the sliding window algorithm, which serves several purposes:
  (1) it guarantees the reliable delivery of data,
  (2) it ensures that data is delivered in order, and
  (3) it enforces flow control between the sender and the receiver.

## Slide 22: Sliding Window Revisited
Sending Side LastByteAcked ≤ LastByteSent LastByteSent ≤ LastByteWritten | Receiving Side LastByteRead < NextByteExpected NextByteExpected ≤ LastByteRcvd + 1

## Slide 23: TCP Flow Control
LastByteRcvd − LastByteRead ≤ MaxRcvBuffer
AdvertisedWindow = MaxRcvBuffer − ((NextByteExpected − 1) − LastByteRead)
LastByteSent − LastByteAcked ≤ AdvertisedWindow
EffectiveWindow = AdvertisedWindow − (LastByteSent − LastByteAcked)
LastByteWritten − LastByteAcked ≤ MaxSendBuffer
If the sending process tries to write y bytes to TCP, but
(LastByteWritten − LastByteAcked) + y > MaxSendBuffer
then TCP blocks the sending process and does not allow it to generate more data.

## Slide 24: Protecting against Wraparound
SequenceNum: 32 bits longs
AdvertisedWindow: 16 bits long
  TCP has satisfied the requirement of the sliding
  window algorithm that is the sequence number
  space be twice as big as the window size (232 >> 2 × 216)
  Packets cannot survive in the Internet for longer than the MSL
  MSL is set to 120 sec
  We need to make sure that the sequence number does not wrap around within a 120-second period of time
  Depends on how fast data can be transmitted over the Internet
Notes: Maximum Segment Lifetime

## Slide 25: Protecting against Wraparound
Notes: Maximum Segment Lifetime

## Slide 26: Keeping the Pipe Full
If the receiver has enough buffer space
  The window needs to be opened far enough to allow a full
  delay × bandwidth product’s worth of data
  Assuming an RTT of 100 ms
Notes: Maximum Segment Lifetime

## Slide 27: Silly Window Syndrome

## Slide 28: Nagle’s Algorithm
If there is data to send but the window is open less than MSS, then we may want to wait some amount of time before sending the available data
But how long?
If we wait too long, then we hurt interactive applications like Telnet
If we don’t wait long enough, then we risk sending a bunch of tiny packets and falling into the silly window syndrome
  The solution is to introduce a timer and to transmit when the timer expires

## Slide 29: Nagle’s Algorithm
We could use a clock-based timer, for example one that fires every 100 ms
Nagle introduced an elegant self-clocking solution
Key Idea
  As long as TCP has any data in flight, the sender will eventually receive an ACK
  This ACK can be treated like a timer firing, triggering the transmission of more data

## Slide 30: Nagle’s Algorithm
When the application produces data to send
if both the available data and the window ≥ MSS send a full segment else if there is unACKed data in flight buffer the new data until an ACK arrives else send all the new data now

## Slide 31: Original Algorithm
Problem
  ACK does not really acknowledge a transmission
    It actually acknowledges the receipt of data
  When a segment is retransmitted and then an ACK arrives at the sender
    It is impossible to decide if this ACK should be associated with the first or the second transmission for calculating RTTs

## Slide 32: Karn/Partridge Algorithm
Associating the ACK with (a) original transmission versus (b) retransmission

## Slide 33: Karn/Partridge Algorithm
Do not sample RTT when retransmitting
Double timeout after each retransmission

## Slide 34: Karn/Partridge Algorithm
Karn-Partridge algorithm was an improvement over the original approach, but it does not eliminate congestion
We need to understand how timeout is related to congestion
  If you timeout too soon, you may unnecessarily retransmit a segment which adds load to the network

## Slide 35: Karn/Partridge Algorithm
Main problem with the original computation is that it does not take variance of Sample RTTs into consideration.
If the variance among Sample RTTs is small
  Then the Estimated RTT can be better trusted
  There is no need to multiply this by 2 to compute the timeout

## Slide 36: Karn/Partridge Algorithm
On the other hand, a large variance in the samples suggest that timeout value should not be tightly coupled to the Estimated RTT
Jacobson/Karels proposed a new scheme for TCP retransmission

## Slide 37: Jacobson/Karels Algorithm
Difference = SampleRTT − EstimatedRTT
EstimatedRTT = EstimatedRTT + (δ × Difference)
Deviation = Deviation + δ (|Difference| − Deviation)
  Where δ is a fraction between 0 and 1
TimeOut = μ × EstimatedRTT + φ × Deviation
  where based on experience, μ is typically set to 1 and φ is set to 4. Thus, when the variance is small, TimeOut is close to EstimatedRTT; a large variance causes the deviation term to dominate the calculation.

## Slide 38: Agenda
Chapter 5. End to End Protocols
E2E Protocols
Simple Demultiplexer (UDP)
Reliable Byte Stream (TCP)
RPC
RTP

## Slide 39: Remote Procedure Call
In Computer Science, a Remote Procedure Call (RPC) is an inter-process communication that allows a computer program to cause a subroutine or procedure to execute in another address space (commonly on another computer on a shared network) without the programmer explicitly coding the details for this remote interaction.
Wikipedia, Nov 2013.
Remote Procedure Call (RPC), that more closely matches the needs of an application involved in a request/reply message exchange.
Peterson 2012

## Slide 40: Remote Procedure Call
When the procedures being called are actually methods of remote objects in an Object-oriented Language.
RPC is known as Remote Method Invocation (RMI)
While the RPC concept is simple, there are two main problems that make it more complicated than local procedure calls:
The network between the calling process and the called process has much more complex properties than the backplane of a computer. For example, it is likely to limit message sizes and has a tendency to lose and reorder messages.
The computers on which the calling and called processes run may have signiﬁcantly different architectures and data representation formats.

## Slide 41: RPC Mechanism
We focus on “RPC Protocol (stack)”
fragments and reassembles large messages (by BLAST)
synchronizes request and reply messages (by CHAN)
dispatches request to the correct process/procedure (by SELECT)

## Slide 42: Request n Reply in RPC

## Slide 43: RPC Implementation
SIMPLE RPC SunRPC DCE-RPC

## Slide 44: Agenda
Chapter 5. End to End Protocols
E2E Protocols
Simple Demultiplexer (UDP)
Reliable Byte Stream (TCP)
RPC
RTP

## Slide 45: Why RTP
Real-time traffic: digitized voice, video, etc.
Experiments with real-time traffic since 1981
Why not existing transport protocols?
UDP: best effort, no guarantee on delay and delay jitter
TCP: long delay and large delay jitter due to retransmission
RPC: designed for interactive exchange of (mostly short) messages

## Slide 46: Requirements for RTP
To be generic and to support different applications (e.g., w/ diff. encoding schemes)
To identify timing relationship among received data;
To synchronize related media streams (e.g., audio & video data streams)
To detect and report packet loss (even though no need for 100% reliability)

## Slide 47: Requirements for RTP
Runs over UDP
Application-Level Framing
  leave application specific details to applications through “profile” and “formats”
    Profile: specifies how to interpret the RTP header information
    Format: specifies how to interpret the data following the RTP header
1) Data packets: specified by RTP
2) Periodic control packets: specified by RTCP (Real-time Transport Control Protocol)

## Slide 48: RTP Header Format

## Slide 49: Bibliography
Kurose, J.F., and Ross, K.W., Computer Networking : A Top-Down Approach Sixth Edition, Pearson Education, Inc. USA, 2013.
Lammle T., Cisco Certified Network Associate : Study Guide Fifth Edition, Sybex, Inc. USA, 2005.
Peterson, L.L., and Davie, B.S., Computer Networks: A Systems Approach Fifth Edition, Morgan Kaufmann, Burlington USA, 2012.
Tanenbaum, A.S., and Wetherall, D.J., Computer Networks Fifth Edition, Pearson Education, Inc., Boston USA, 2011.

## Slide 50: THANK YOU
Gandeva Bayu Satrya (GBS)
gbs@ittelkom.ac.id
gandeva.bayu.s@gmail.com
TELKOM ENGINEERING SCHOOL
Telkom University