## Slide 1: Chapter 3 Internetworking
Gandeva Bayu Satrya (GBS)
gbs@ittelkom.ac.id
gandeva.bayu.s@gmail.com
TELKOM ENGINEERING SCHOOL
Telkom University

## Slide 2: Agenda
Chapter 3. Internetworking
3.1 Switching and Bridging
VCI, bridge (STP)
3.2 Basic Internetworking
Class IP, Subneting, ARP, DHCP, ICMP
3.3 Routing
Routing, Distance Vector, Link State

## Slide 3: Switching and Forwarding
SWITCH
A mechanism that allows us to interconnect links to form a large network.
A multi-input, multi-output device which transfers packets from an input to one or more outputs.
Every host on a switched network has its own link to the switch.
A switch’s primary job is to receive incoming packets on one of its links and to transmit them on some other link

## Slide 4: Switching and Forwarding
How does the switch decide which output port to place each packet on?
It looks at the header of the packet for an identifier that it uses to make the decision
Two common approaches
Datagram or Connectionless Approach.
Virtual circuit or Connection-oriented Approach.
A third approach source routing is less common.

## Slide 5: a. Datagram Approach
    Every packet contains enough information to enable any switch to decide how to get it to destination
    To decide how to forward a packet, a switch consults a forwarding table (sometimes called a routing table)
Destination Port
-------------------------
A 3
B 0
C 3
D 3
E 2
F 1
G 0
H 0
Forwarding Table for Switch 2

## Slide 6: MAC Add Table in CISCO
GBS_SW#sh mac-address-table
Mac Address Table
-------------------------------------------
Vlan Mac Address Type Ports
---- ----------- -------- -----
1 0009.7cba.c915 DYNAMIC Fa0/1
1 000b.be7a.69bc DYNAMIC Fa0/3
1 0030.a368.e65a DYNAMIC Fa0/1
1 0060.2f58.3453 DYNAMIC Fa0/4
1 0060.5c94.ee01 DYNAMIC Fa0/1
1 0060.7083.2b34 DYNAMIC Fa0/1
1 00e0.a3bc.03a8 DYNAMIC Fa0/2
GBS_SW#
Which CLIENT...?
Notes: Question :
Berapakah MAC-add untuk PC-2 (bawah)???

## Slide 7: b. Virtual-Circuit Approach
Virtual Circuit Switching
  Widely used technique for Packet Switching
  Uses the concept of Virtual Circuit (VC)
  Also called a connection-oriented model
  First set up a virtual connection from the source host to the destination host and then send the data

## Slide 8: VCI
 | In Int | In VCI | Out Int | Out VCI
SW-1 | 2 | 5 | 1 | 11
SW-2 | 3 | 11 | 2 | 7
SW-3 | 0 | 7 | 1 | 4

## Slide 9: Switching and Forwarding
Comparison with the Datagram Model
Datagram network has no connection establishment phase and each switch processes each packet independently
Each arriving packet competes with all other packets for buffer space
If there are no buffers, the incoming packet must be dropped
In VC, we could imagine providing each circuit with a different quality of service (QoS)
The network gives the user some kind of performance related guarantee
Most popular examples of VC technologies are Frame Relay and ATM
One of the applications of Frame Relay is the construction of VPN

## Slide 10: Switching and Forwarding
ATM (Asynchronous Transfer Mode)
  Connection-oriented packet-switched network
  Packets are called cells
    5 byte header + 48 byte payload
  Fixed length packets are easier to switch in hardware
    Simpler to design
    Enables parallelism

## Slide 11: Switching and Forwarding
ATM
  User-Network Interface (UNI)
    Host-to-switch format
    GFC: Generic Flow Control
    VCI: Virtual Circuit Identifier
    Type: management, congestion control
    CLP: Cell Loss Priority
    HEC: Header Error Check (CRC-8)
  Network-Network Interface (NNI)
    Switch-to-switch format
    GFC becomes part of VPI field

## Slide 12: c. Source Routing
Source Routing
All the information about network topology that is required to switch a packet across the network is provided by the source host

## Slide 13: Agenda
Chapter 3. Internetworking
3.1 Switching and Bridging
VCI, bridge (STP)
3.2 Basic Internetworking
Class IP, Subneting, ARP, DHCP, ICMP
3.3 Routing
Routing, Distance Vector, Link State

## Slide 14: Bridges and LAN Switches
Class of switches that is used to forward packets between shared-media LANs such as Ethernets
Known as LAN switches
Referred to as Bridges
Suppose you have a pair of Ethernets that you want to interconnect
One approach is put a repeater in between them
An alternative would be to put a node between the two Ethernets and have the node forward frames from one Ethernet to the other
  This node is called a Bridge
  A collection of LANs connected by one or more bridges is usually said to form an Extended LAN

## Slide 15: Bridges and LAN Switches
Strategy works fine if the extended LAN does not have a loop in it
Why?
  Frames potentially loop through the extended LAN forever
  B1, B4, and B6
  B1, B2, B3, and B5
  B1, B5, and B7

## Slide 16: Bridges and LAN Switches
How does an extended LAN come to have a loop in it?
Network is managed by more than one administrator
  For example, it spans multiple departments in an organization
Loops are built into the network to provide redundancy in case of failures
Solution :
Spanning Tree Algorithm
Switch with Spanning Tree Protocol (STP)

## Slide 17: Spanning Tree Algorithm
Algorithm selects ports as follows:
  Each bridge has a unique identifier
  Elect the bridge with the smallest id as The Root of the spanning tree
  The root bridge always forwards frames out over all of its ports
  Each bridge computes the shortest path to the root and notes which of its ports is on this path
  Finally, all the bridges connected to a given LAN elect a single designated bridge that will be responsible for forwarding
  Each LAN’s designated bridge is the one that is closest to the root
  If two or more bridges are equally close to the root, smallest id
  Each bridge is connected to more than one LAN

## Slide 18: Spanning Tree Algorithm
B1 is the root bridge
B3 and B5 are connected to LAN A, but B5 is the designated bridge
B5 and B7 are connected to LAN B, but B5 is the designated bridge

## Slide 19: Spanning Tree Algorithm
Even after the system has stabilized, the root bridge continues to send configuration messages periodically
  Other bridges continue to forward these messages
When a bridge fails, the downstream bridges will not receive the configuration messages
After waiting a specified period of time, they will once again claim to be the root and the algorithm starts again

## Slide 20: Agenda
Chapter 3. Internetworking
3.1 Switching and Bridging
VCI, bridge (STP)
3.2 Basic Internetworking
Class IP, Subneting, ARP, DHCP, ICMP
3.3 Routing
Routing, Distance Vector, Link State

## Slide 21: Internetworking
  Internetworking…
  is An arbitrary collection of networks interconnected (IP) to provide some sort of host-host to packet delivery service.
CISCO, 2008
Notes: Difference internet and Internet???
We use the term internetwork, or sometimes just internet with a lowercase i, to refer to an arbitrary collection of networks interconnected to provide some sort of host-to-host packet delivery service. For example, a
corporation with many sites might construct a private internetwork by interconnecting the LANs at their different sites with point-to-point links leased from the phone company.
When we are talking about the widely used global internetwork to which a large percentage of networks are now connected, we call it the Internet with a capital I.

## Slide 22: Assigning Addresses
Describe the process for requesting IP public addresses, the role ISPs play in the process, and the role of the regional agencies that manage IP address registries
Notes: An IP address is an address used to uniquely identify a device on an IP network. The address is made up of 32 binary bits which can be divisible into a network portion and host portion with the help of a subnet mask.

## Slide 23: Internet Protocols
What is IP
  IP stands for Internet Protocol
  Key tool used today to build scalable, heterogeneous internetworks
  It runs on all the nodes in a collection of networks and defines the infrastructure that allows these nodes and networks to function as a single logical internetwork
Internet Protocols
  IPv4
  IPv6 (wait... chapter 4)

## Slide 24: IP Fragmentation & Reassembly
Each network has some MTU (Maximum Transmission Unit)
  Ethernet (1500 bytes), FDDI (4500 bytes)
Strategy
  Fragmentation occurs in a router when it receives a datagram that it wants to forward over a network which has (MTU < datagram)
  Reassembly is done at the receiving host
  All the fragments carry the same identifier in the Ident field
  Fragments are self-contained datagrams
  IP does not recover from missing fragments

## Slide 25: IP Fragmentation & Reassembly

## Slide 26: Role of IPv4 Protocols
CISCO, 2008

## Slide 27: IPv4 Format

## Slide 28: IPv4 Class

## Slide 29: IPv4
Define public address and private address
The private address blocks are:
10.0.0.0 to 10.255.255.255 (10.0.0.0 /8)
172.16.0.0 to 172.31.255.255 (172.16.0.0 /12)
192.168.0.0 to 192.168.255.255 (192.168.0.0 /16)

## Slide 30: IPv4 Convert

## Slide 31: Subnetting
Subnetting provides a ﬁrst step to reducing total number of network numbers that are assigned.
  Easy for Managed and Decrease of Using IP.
Add another level to address/routing hierarchy: subnet
What is…
Network/Subnet : ID parent
Host/client/node : Childs
Gateway (GW) : IP add on Router (1st allocation IP)
Broadcast (BC) : IP add on Switch (Last allocation IP)
Prefix/ “/” : how many bit are Used (#of bit 1)
Subnet Mask (SM) : Binary of Prefix

## Slide 32: Subnetting
How many Subnet and Hosts?
Number of subnets available=
2number-of-bits-1
(***subnet zero and subnet extended***)
Number of hosts per subnet available=
2number-of-bits-0-2
(***gateway and broadcast***)

## Slide 33: Subnetting (Ex.1)
CCNA International Exam, 2012
Given the address 192.168.20.19/28, which of the following are valid host addresses on this subnet?
A. 192.168.20.29
B. 192.168.20.16
C. 192.168.20.17
D. 192.168.20.31
E. 192.168.20.0
11111111. 11111111. 11111111.11110000
^
24=16
192.168.20.16 ………………………………………………. 192.168.20.31
.17 .30

## Slide 34: Subnetting (Ex.2)
Refer to the exhibit. The user at Workstation B reports that Server A cannot be reached. What is preventing Workstation B from reaching Server A?
A. The IP address for Server A is a broadcast address.
B. The IP address for Workstation B is a subnet address.
C. The gateway for Workstation B is not on the same subnet.
D. The gateway for Server A is not on the same subnet.
CCNA International Exam, 2012

## Slide 35: Subnetting (Ex.3)
Refer to the exhibit. All of the routers in the network are configured with the IP Subnet-Zero command. Which network addresses should be used for Link A and Network A? (Choose two.)
A. Network A - 172.16.3.48/26
B. Network A - 172.16.3.128/25
C. Network A - 172.16.3.192/26
D. Link A - 172.16.3.0/30
E. Link A - 172.16.3.40/30
F. Link A - 172.16.3.112/30
CCNA International Exam, 2012

## Slide 37: Supernetting
Supernetting/CIDR/VLSM
Classless Inter-Domain Routing
Variable Length Subnet Mask
Prefix Aggregation a.k.a. Route Summarization
  A technique that addresses two scaling concerns in the Internet
    The growth of backbone routing table as more and more network numbers need to be stored in them
    Potential exhaustion of the 32-bit address space
  Address assignment efficiency
    Arises because of the IP address structure with class A, B, and C addresses

## Slide 38: Supernetting [Ex.1]
CISCO, 2008

## Slide 39: Supernetting
192.168.0.0/23 00000000
192.168.2.0/23 00000010
192.168.4.0/22 00000100
192.168.8.0/21 00001000
---------------------------------------
00000000
192.168.0.0/20  Route Summarization

## Slide 40: Supernetting [Ex.2]

## Slide 41: Agenda
Chapter 3. Internetworking
3.1 Switching and Bridging
VCI, bridge (STP)
3.2 Basic Internetworking
Class IP, Subneting, ARP, DHCP, ICMP
3.3 Routing
Routing, Distance Vector, Link State

## Slide 42: ARP
Map IP addresses into physical addresses
  destination host
  next hop router
Techniques
  encode physical address in host part of IP address
  table-based
ARP (Address Resolution Protocol)
  table of IP to physical address bindings
  broadcast request if IP address not in table
  target machine responds with its physical address
  table entries are discarded if not refreshed (ARP cache)

## Slide 43: DHCP
Drawbacks of manual configuration
  A lot of work to configure all the hosts in a large network
  Configuration process is error-prune
Automated Configuration Process is required
DHCP server is responsible for providing configuration information to hosts
There is at least one DHCP server for an administrative domain
DHCP server maintains a pool of available addresses

## Slide 44: ICMP
Internet Control Message Protocol (ICMP)
Defines a collection of error messages that are sent back to the source host whenever a router or host is unable to process an IP datagram successfully
  Destination host unreachable due to link /node failure
  Reassembly process failed
  TTL had reached 0 (so datagrams don't cycle forever)
  IP header checksum failed
ICMP-Redirect
  From router to a source host
  With a better route information

## Slide 45: Agenda
Chapter 3. Internetworking
3.1 Switching and Bridging
VCI, bridge (STP)
3.2 Basic Internetworking
Class IP, Subneting, ARP, DHCP, ICMP
3.3 Routing
Routing, Distance Vector, Link State

## Slide 46: Routing
  Forwarding versus Routing
    Forwarding:
      to select an output port based on destination address and routing table
    Routing:
      process by which routing table is built

## Slide 47: Routing Table
  Forwarding table VS Routing table
    Forwarding table
      Used when a packet is being forwarded and so must contain enough information to accomplish the forwarding function
      A row in the forwarding table contains the mapping from a network number to an outgoing interface and some MAC information, such as Ethernet Address of the next hop
    Routing table
      Built by the routing algorithm as a precursor to build the forwarding table
      Generally contains mapping from network numbers to next hops

## Slide 48: Example
  Example rows from (a) routing and (b) forwarding tables

## Slide 49: Routing Example
  Network as a Graph
  The basic problem of routing is to find the lowest-cost path between any two nodes
    Where the cost of a path equals the sum of the costs of all the edges that make up the path.

## Slide 50: Routing Protocol

## Slide 51: Routing Protocol Evolution

## Slide 52: Agenda
Chapter 3. Internetworking
3.1 Switching and Bridging
VCI, bridge (STP)
3.2 Basic Internetworking
Class IP, Subneting, ARP, DHCP, ICMP
3.3 Routing
Routing, Distance Vector, Link State

## Slide 53: Distance Vector
Each node constructs a one dimensional array (a vector) containing the “distances” (costs) to all other nodes and distributes that vector to its immediate neighbors.
Starting assumption is that each node knows the cost of the link to each of its directly connected neighbors.
Each router maintains a table of [Destination, Cost, NextHop] tuples, and exchanges a list of (Destination, Cost) pairs with its directly connected neighbors.

## Slide 54: Distance Vector

## Slide 55: Distance Vector

## Slide 56: Distance Vector
COMPLETE

## Slide 57: DV Example : RIP
R1# show ip route 172.16.0.0/30 is subnetted, 2 subnets R 172.16.1.164 [120/1] via 172.16.1.162, 00:00:09, FastEthernet0/0 C 172.16.1.160 is directly connected, FastEthernet0/0 R 172.18.0.0/16 [120/1] via 172.16.1.162, 00:00:09, FastEthernet0/0 R 192.168.4.0/24 [120/2] via 172.16.1.162, 00:00:09, FastEthernet0/0 10.0.0.0/30 is subnetted, 1 subnets C 10.10.10.16 is directly connected, Serial1/0 192.168.1.0/27 is subnetted, 1 subnets C 192.168.1.0 is directly connected, Loopback1 R 192.168.2.0/24 [120/1] via 172.16.1.162, 00:00:11, FastEthernet0/0 R 192.168.3.0/24 [120/1] via 10.10.10.18, 00:00:03, Serial1/0
R1(config)# router rip
R1(config-router)# net 192.168.1.0
R1(config-router)# net 172.16.1.160
R1(config-router)# net 10.10.10.16

## Slide 58: Link State Routing
Each node is assumed to be capable of finding out the state of the link to its neighbors (up or down) and the cost of each link.
Every node knows how to reach its directly connected neighbors, and if we make sure that the totality of this knowledge is disseminated to every node, then every node will have enough knowledge of the network to build a complete map of the network.

## Slide 59: Link State Routing
Reliable Flooding
Flooding of link-state packets. (a) LSP arrives at node X; (b) X floods LSP to A and C; (c) A and C flood LSP to B (but not X); (d) flooding is complete

## Slide 60: Shortest Path Routing
The algorithm works as follows:
Initialize the Confirmed list with an entry for myself; this entry has a cost of 0.
For the node just added to the Confirmed list in the previous step, call it node Next and select its LSP.
For each neighbor (Neighbor) of Next, calculate the cost (Cost) to reach this Neighbor as the sum of the cost from myself to Next and from Next to Neighbor.
If the Tentative list is empty, stop. Otherwise, pick the entry from the Tentative list with the lowest cost, move it to the Confirmed list, and return to step 2.

## Slide 61: Shortest Path Routing

## Slide 62: LS Example : OSPF
R1# sh ip route
172.16.0.0/30 is subnetted, 2 subnets
O 172.16.1.164 [110/2] via 172.16.1.162, 00:00:02, FastEthernet0/0
C 172.16.1.160 is directly connected, FastEthernet0/0
172.18.0.0/30 is subnetted, 1 subnets
O IA 172.18.1.0 [110/65] via 172.16.1.162, 00:00:02, FastEthernet0/0
192.168.4.0/32 is subnetted, 1 subnets
O IA 192.168.4.1 [110/66] via 172.16.1.162, 00:00:02, FastEthernet0/0
10.0.0.0/30 is subnetted, 1 subnets
C 10.10.10.16 is directly connected, Serial1/0
192.168.1.0/27 is subnetted, 1 subnets
C 192.168.1.0 is directly connected, Loopback1
192.168.2.0/32 is subnetted, 1 subnets
O 192.168.2.1 [110/2] via 172.16.1.162, 00:00:04, FastEthernet0/0
192.168.3.0/32 is subnetted, 1 subnets
O 192.168.3.1 [110/3] via 172.16.1.162, 00:00:06, FastEthernet0/0

## Slide 63: Task Chapter 3
[Bahasa/handwriting]
[Deadline-03/10/13]
[12.01pm]
No. 1 : Exercise Chapter 3, Peterson 5th Ed. Page 294, no. 46!
No. 2 : Exercise Chapter 3, Peterson 5th Ed. Page 295, no. 48!

## Slide 64: Bibliography
Kurose, J.F., and Ross, K.W., Computer Networking : A Top-Down Approach Sixth Edition, Pearson Education, Inc. USA, 2013.
Lammle T., Cisco Certified Network Associate : Study Guide Fifth Edition, Sybex, Inc. USA, 2005.
Peterson, L.L., and Davie, B.S., Computer Networks: A Systems Approach Fifth Edition, Morgan Kaufmann, Burlington USA, 2012.
Tanenbaum, A.S., and Wetherall, D.J., Computer Networks Fifth Edition, Pearson Education, Inc., Boston USA, 2011.

## Slide 65: THANK YOU
Gandeva Bayu Satrya (GBS)
gbs@ittelkom.ac.id
gandeva.bayu.s@gmail.com
TELKOM ENGINEERING SCHOOL
Telkom University